## Slide 1
v3

## Slide 2: Agenda
Network Screening
Systemic Treatments
$1.5 Million for 2021 Deployment of Enhanced Signing, Pavement Markings & Cameras
Initial results after 1 year

## Slide 3: Level of Effort for WWD

## Slide 4: After collection WWD Data for 10 years with $0 budget…
I got $1.5 Million of HSIP funding for enhanced signing and pavement markings.
This Photo by Unknown Author is licensed under CC BY-NC

## Slide 5: Where to Spend?
?
467 Interchanges in Iowa

## Slide 6: Network Screening
By Dr. Huaguo Zhou & Md Atiquzzaman of Auburn University
https://journals.sagepub.com/doi/pdf/10.1177/0361198118783152

## Slide 7: Iowa’s Modification Scoring System

## Slide 8: Started with 472 interchanges and then Multiplied by 100 “points”
47,200 Available Points in the Pool

## Slide 9: Distribution of Points
Crashes (25%) - 11,800 points
Volume (25%) – 11,800 points
  Mainline (12.5%)
  Sideroad (12.5%)
Geometry (25%) – 11,800 Points
Urban/Rural (20%) – 9,440 Points
Non-Crash WWD Events (5%) – 2,360 Points

## Slide 10: Don’t forget about At-Grades
These were not part of the network screening

## Slide 12: Common Philosophy for Signs
Larger signs
  36” x 36”  48” x 48” (78% increase)
Strategically Placed
  Install sign where a potential WWD is looking
  Stop placing signs where it is convenient
    (like on the back of Stop sign)
Aim (angle) the sign for intended audience
  Think about who (why) you are doing this.
Left and Right sides
  2 is better than 1

## Slide 13: At-Grade Intersection
New Signs/Pavement Markings
Larger Signs
Strategically placed & aimed
New
New
New
New
New
New
New
New
Larger
Larger
UAC
UAC

## Slide 15
Before (MUTCD)
Good (w/ Systemic Treatments)

## Slide 16: Had a few WWD, but this one…

## Slide 17: 1 mile further down the road…
Was stopped by Police
Blood Alcohol Concentration (BAC) = 0.206

## Slide 18
Good (w/ Systemic Treatments)
Better (I think)… w/ Text Version of Keep Right
Added 6/1/23
Red Conspicuity sheeting on Do Not Enter Legs also

## Slide 19: Level of Effort for WWD
BAC
0.000
0.300
???

## Slide 20: Standard Diamond Interchange

## Slide 22: Be Careful with Do Not Enter & Stop Signs
Do Not Enter
Was Blocking the STOP Sign.
We fixed by moving DNE out further.

## Slide 23: Folded Diamond Interchange

## Slide 24
“Gateway” for Folded Diamonds
Interesting Countermeasure #1

## Slide 28
Zac’s Sign

## Slide 29: Hypothesis….
If you can solve the WWD problem for Daytime, non-drunks…. (85% that self correct)…. Will it reduce the nighttime intoxicated WWD problem, (the other 15%)?
?
?
?
?
Probably Not

## Slide 30: Preliminary Results (Interstates, Freeways & Expressways) With a speed limit of 60, 65 or 70 MPH Currently too hard to review 55 MPH highways
2023 (as of 6/20) 10 crashes
  Only 1 might have been at a location that had systemic countermeasures
    BAC unknown
  4 with BAC (Average was 0.194)
2022 19 crashes
  Only 4 may have been from a location with systemic countermeasures
  Only 1 (of the 4) recorded a BAC. It was 0.144
  6 with a BAC (Average was 0.176)
2021 8 Crashes
  None from a location with Systemic Countermeasures
  4 w/ a BAC (Average was 0.147)

## Slide 31: To wrap things up, there is 1 more thing that I’d like you to know and share with your family, friends and co-workers.

## Slide 32
Questions?